## Slide 1: An Update on NHDPlus
July 9, 2013
Tommy Dewald Cindy McKay
EPA Office of Water Horizon Systems Corporation
1987
2010

## Slide 2: Overview
NHDPlus Concepts
Flow Estimation Projects
Higher Resolution NHDPlus
Integrating Z-value
WBD HUC12 network relationships with NHDPlus

## Slide 3: Business Need
‘All the water that will ever be is, right now.’
- National Geographic, October 1993
‘We forget that the water cycle and the life cycle are one.’
- Jacques Cousteau
To know where surface waters and things affecting them are located (anywhere on the landscape) in order to support measures of progress towards providing clean and safe water.

## Slide 4: NHD & NHDPlus Concepts
National Hydrography Dataset (NHD)
  National digital map of Nation’s waterbodies
  Stream addresses (like street addresses) for linking features to the stream network
  Stream network that enables hydrological analysis of features
National Hydrography Dataset Plus (NHDPlus)
  Extends the capabilities of the NHD by integrating the network with the land surface
  Associates each the NHD stream segment with its local drainage area (catchment)
  Stream and catchment characteristics

## Slide 5: National Hydrography Dataset Plus (NHDPlus)
Developed by EPA and USGS-Water (2006) to provide flow volume and velocity estimates for pollution dilution modeling
    Builds upon NHD stream network – integrated with elevation and HUC12s
    Additional stream attributes (stream order, flow, etc)
    Catchments and attributes (precipitation, temperature, land cover)
Success of initial version led to Version 2 production by EPA and USGS-Water
NHDPlus team
  EPA - Tommy Dewald, Cindy McKay (c), Tim Bondelid (c)
  USGS-Water - Rich Moore, Craig Johnston, Al Rea, [Greg Schwarz, Kernell Ries, Dave Wolock]

## Slide 6
Elevation
(30m)
Hydrologic Units
(HUC12)
Stream Network
NHDPlus provides the Surface Water Geospatial Framework
Stream Network | Map Scale | Map Accuracy | Total Stream Miles (mi) | # of Stream Segments | Stream Segment Average Length (mi) | # of Lakes | Catchment Average Area (sq mi)
Reach File Version 1 (RF1) | 1:500K | +/- 254m | 600,000 | 60,000 | 10 | 4,100 | 50
Medium Resolution NHD | 1:100k | +/- 50m | 3,200,000 | 2,600,000 | 1.2 | 38,000 | 1.1
High Resolution NHD | 1:24K or better | +/- 12m | 7,500,000 | 20,000,000 | 0.37 | 537,000 | do not exist
NHDPlus catchments tie the landscape to the stream network forming a ‘surface water geofabric’
(These figures are approximations (+/- 10%) provided for purposes of comparison.)

## Slide 7: NHDPlus Concepts: Integrating the Landscape with the Stream Network
NHDPlus Catchments in 3D

## Slide 8
Introducing
NHDPlus Version 2
Significant Version 2 improvements:
Over 5,000 isolated networks connected
Over 60% enhanced elevations nationally
Now-completed national HUC12s
More robust flow estimation method
  Runoff (USGS water balance model)
  Excess evapotranspiration
  Reference Gage Regression
  Flow additions and removals
  Adjustment using gaged flows
“By Endurance We Conquer”
(Sir Ernest Shackleton)
2012 ESRI UC
October 15, 2012

## Slide 9: Estimating Streamflow Using NHDPlus
  Mean annual flow and velocity (completed as part of NHDPlus)
  Mean monthly flow (completion during FY2013 as part of NHDPlus)
  7Q10 flows (completion during FY2013 by EPA OPP and OW)
  On-Going: Mean daily flows (planned by USGS Water Census)
  Vision: Forecasting future flows (substituting forecasted model inputs)
  How can we improve our stream periodicity characteristics?
“What I think this project (NHDPlus) offers that is unique is in the full characterization of the flow network, identification of unregulated and regulated gages and reaches, and network-based interpolation and adjustment of flows.” (A.Rea, USGS)

## Slide 10: Higher Resolution NHDPlus
  Efforts to date
    Value-Added Attributes only – Texas, Vermont, Nebraska
    NHDPlus – Minnesota, New York City watershed (LiDAR-based), outstanding proposal for an area in Alaska (IfSAR-based)
    USGS high resolution NHD network improvement project (and plans for network value-added attributes (FY14), catchments and flow estimates)
  Interest in LiDAR-based hydrography
    LiDAR-NHD Best Practices Workgroup report (pending)
    Hope to more fully address extraction of hydrologic features in USGS LiDAR collection specification and ASPRS LiDAR Manual
  Also, potential for hybrid solutions using high resolution NHD with medium resolution NHDPlus
  How can we improve our stream periodicity characteristics?

## Slide 11: Higher Resolution NHDPlus
  Minnesota: Mississippi Headwaters
  NHD 1:100K -> 1:8K
  DEM 30M -> 3M
  NHD 1:100K -> 1:24K
  NED 30M -> 10M
  NYC: Drinking Water Source Area
  Hybrid: High Res NHD
  With NHDPlusV2 Catchments

## Slide 12: Linking WBD HUC12 to the NHDPlusV2 Network
  WBD HUC12 boundaries define the ridge lines of NHDPlusV2 catchments.
  WBD: 87,259 HUC12s – avg. size of 72.2 sq. mi.
  NHDPlusV2: 2,647,454 Catchments – avg. size of 1.2 sq. mi.
  Can we roll catchments up to HUC12s?

## Slide 13: NHDPlusV2 Catchments-HUC12 Comparison
Using GRID processing, overlay the catchments on the HUC12s and assign each catchment to the HUC12 that contains most of the catchment
Identify the parts of catchments that extend outside of the HUC12 that the catchment has been assigned to. These cells are colored red on the comparison map.
For the country, 97% of the cells are assigned to the correct HUC12.

## Slide 14
97.0 % agreement between aggregated NHDPlus catchments and WBD HUC 12s
(Red = areas of disagreement)

## Slide 15: NHDPlusV2 Catchments-HUC12 Comparison
Of the 3%, The Most Common Areas of Disagreement

## Slide 16: NHDPlusV2 Catchments-HUC12 Comparison
Large Areas of Disagreement

## Slide 17: NHDPlusV2 Catchments & HUC12 2 Linked Analysis Scales
  NHDPlusV2
  2,647,454 Catchments
  Avg. size - 1.2 sq. mi.
  WBD
  87,259 HUC12s
  Avg. size - 72.2 sq. mi.

## Slide 18: NHDPlusV2 - Other News
NHDPlus V1 -> V2 Crosswalk published
WBD HUC12 – NHDPlusV2 Catchment Crosswalk soon to be published
47,000 dams linked to the NHDPlus network
USGS Proposal for z-values still seeking funding

## Slide 19: Summary
NHDPlus provides the common geospatial surfacewater framework (the plumbing)
NHDPlus is the closest we’ve come to a hydro Geo-fabric
NHDPlus continues to grow in data content and analysis capabilities
Enabling informed decision-making

## Slide 20: Thanks!
EPA GIS Workgroup Meeting
Arlington, VA - May 7, 2009
http://www.wordle.net