## Slide 1: Building Analytical Applications Using NHDPlusV2
Presented by:
Cindy McKay
Horizon Systems Corporation
Sponsored by:
US EPA, Office of Water

## Slide 2: Agenda
NHDPlus Basics
Elements of an NHDPlusV2 Application
Resources

## Slide 3: NHDPlusV2 Basics
National
Hydrography
Dataset (NHD)
Watershed
Boundary
Dataset (WBD)
National
Elevation
Dataset (NED)

## Slide 4: NHDPlusV2 Basics
NED
Elevation

## Slide 5: NHDPlusV2 Basics
WBD
HUC 12 Boundaries
___________
Used To Build
Walls
In the Elevation

## Slide 6: NHDPlusV2 Basics
NHD Streams and Waterbodies
___________
Used to Trench
And Scoop
Into the Elevation

## Slide 7: NHDPlusV2 Basics
Catchment
for each Network Segment
Link the mapped surface water to the landscape.

## Slide 8: NHDPlusV2 Components
Vectors
Rasters
Many Attributes
NED Snapshot
FDR/FAC
Hydro DEM
Catchments
More…
NHD Snapshot
WBD Snapshot
Hydro-Enforcement Features
Catchment Polys

## Slide 9: Elements of an NHDPlus Application
NHDPlus Surface Water Network and Catchments
NHDPlus Network Attributes
Points of Interest Linked the Network
Catchment & Watershed Attributes
Network Navigation and Information Discovery
Analysis

## Slide 10: NHDPlus Surface Water Network Features and Catchments
NHDFlowlines
  Streams and other flow paths
NHDWaterbody
  Lakes, ponds, swamps and other discrete waterbodies
NHDArea
  Polygonal versions of features in NHDFlowline
Catchments
  Elevation based area that drains to an individual NHDFlowline feature

## Slide 11: NHDPlus Network Attributes
Stream Order
Distance to Network Terminus
Cumulative Network Length Upstream
Catchment Area & Cumulative Drainage Area
Elevation & Slope
Level Path ID
Terminal Path ID

## Slide 12: Points of Interest along the Network (NHDPlus, Yours & Others)
Stream Flow Gages (NHDPlus)
Dams (NHDPlus)
Water Quality Monitoring Stations, Discharge Permits, WQ Standards, Assessments, Impairments, and TMDLs (EPA)
Road Crossings
Habitats
…

## Slide 13: Linking Information to the NHDPlus Network
Reach 07010102000236
Measure 85.28949
100
0
ComID 72854635
Measure 85.28949

## Slide 14: Catchment & Drainage Area Attributes (NHDPlus)
Mean Annual & Monthly Temperature
Mean Annual & Monthly Precipitation
Mean Annual & Monthly Runoff
NLCD 2011 – Land Use, Impervious Surface, 2001/2006/2011 Change

## Slide 15: Catchment & Drainage Area Characteristics (Yours)
Raster Formats:
Grid, .img, .tif, .bmp, .png, .jpg, or .gif
Raster Value Type:
Continuous Numerical or Categorical

## Slide 16: Navigating the Network
NHDPlus Data:
  NHDPlus Network Value Added Attributes
  NHDPlus Flow Table
  Geometric Network & ArcGIS
Tools:
  Flow Table Navigator
  Network VAA Navigator

## Slide 17: Navigating the Network
NHDPlus Network Value Added Attributes
Level Path Identifier

## Slide 18: Navigating the Network
NHDPlus Network Value Added Attributes
Terminal Path Identifier

## Slide 19: Navigating the Network
NHDPlus PlusFlow Table
1
3
2
4
5
FromID | ToID
1 | 5
3 | 2
4 | 2
2 | 5

## Slide 20: Navigating the Network
NHDPlus Network Value Added Attributes
N1
N2
N3
N4
N5
From and To Node Numbers

## Slide 21: Navigating the Network
5
4
3
2
1
Hydrologic Sequence Numbers
NHDPlus Network Value Added Attributes

## Slide 22: Navigating the Network with NHDPlus Flow Table Navigator
NHDPlusV2 Flow Navigator

## Slide 23: Navigating the Network with NHDPlusV2 Network VAA Navigator
NHDPlusV2 VAA Navigator
Navigation Results Layer

## Slide 24: Navigating the Network with NHDPlusV2 Network VAA Navigator

## Slide 25: Navigating the Network with NHDPlusV2 Network VAA Navigator
Upstream until
drainage area < 50 sqkm

## Slide 26: Discovering data linked to the network

## Slide 27: Discovering Data Linked to the Network
WQ Monitoring Station
Drinking Water Intake
Stream Flow Gage
Rug Rat Habitat
Impaired Waters
Timber Production
S
Paper Mill Discharge Permit

## Slide 28: Basin Delineation

## Slide 29: Basin Delineation

## Slide 30: Basin Delineation

## Slide 31: Analysis
Fate/Transport Modeling
Dilution Modeling
Impact Analysis
Watershed Characterization
Proximity Studies
…

## Slide 32: Resources
NHDPlus.com
  Data
  Tools
  Documentation
  Exercises/Tutorials
  Presentations
  Links to NHDPlus Applications and Authors
DEAR NHDPLUS@HSCNET.COM,